## Slide 2
On-Train Driver Console
HQ Train Monitoring HMI

## Slide 3
Operation Scenario 1(Red+Gray blinking) :
Train power : OFF
Train speed: 0 km/h
Input current: 0A
Operation Scenario 2(Orange) :
Train power : ON ,
Train speed : low (0 km/ h – 20km/h)
Input current: 10 ~ 20 A
Operation Scenario 2(Green) :
Train power : ON ,
Train speed : Running (56 km/ h – 90 km/ h)
Input current : 140A ~ 180A
Operation Scenario 4(Red + Alert) :
Train power : OFF
Train speed: 0 km/h
Input current: 0A

## Slide 4
Railway third track 750V DC
Train front radar detection area
Train driving
DC motor
Third track power block Input control breakers
Train input electric current meter
2D Train in physical world simulation
Real-world train module function mapping
Third track block power control PLC
Train driving control PLC
Train onboard RTU
On-Train Modbus-TCP Link
On-Train S7comm Bus
Train Driver Console [ on Train ]
On train antenna
Railway train communication antenna
On train Emergency power control breaker
HQ Trains Operation & Monitor HMI
Railway SCADA Modbus-TCP Link
Wireless connection
Train input power control breaker
3rd track power to train link
Train front radar
Train front signal state receiver
Train input electric voltage meter
Train speed meter
Air Brake Pressure meter
Railway SCADA S7comm Link
Electrical Signal to PLC
latching relay or switch
Sensors and meters
Electrical Signal to RTU
DC power link

## Slide 5
Railway Physical-world Simulator
10.0.10.12X
Coils set request
10 PLC coils state (output to 3rd track power switch)
Railway HQ Trains Monitor HMI(s)
10 train front radar state ( input to PLC)
20 PLC coils ( output to moto and brake)
HMI network 192.168.10.x
Railway Modbus 192.168.100.0/24
RTU Memory data
Users
Railway engineer
Railway 3rd tack power switches control PLC network
PLC-06
PLC-07
[Slave, Slot-1] I/O: 0/2
[Master, Slot-0]
I/O: 0/8
On train operation control PLC network
PLC-11
PLC-12
[Slave, Slot-1] I/O: 2/4
[Master, Slot-0]
I/O: 8/16
10.0.10.13X
RTU 00 - 09
On train RTU network
Electrical signal communication simulation module (10.0.10.100)
50 RTU input ( trains throttle, brake, voltage, current ,speed sensors)
Serial Comm link between PLC and RTU
Register read request and Coils set request
Train driver consoles
Train drivers
Trains Modbus 192.168.101.0/24
Railway S7Comm bus 192.168.102.0/24
0
1
2
3
4
5
6
7
9
Train S7Comm bus 192.168.101.0/24

## Slide 6
Front radar detection area
Front detection sensor
Speed sensor
Throttle & break
HR0
Coil00
Coil01
Overall train
power
HR1
Front sensor state holding register
Speed sensor state holding register
Coil output to throttle
Coil output to train brake
Train HMI control panel
Modbus command
Train Auto control logic
Modbus data

## Slide 8
Train ID
Train current speed gauge
Train average speed display
Current throttle state indicator
Manual throttle control slider
Current brake state indicator
Manual brake control slider
Train Control PLC information
PLC Input contact ID and State
PLC output coil ID
Train air brake pressure gauge
Manual control enable checkbox
Train current operation state
Train moving direction control
Train max speed configuration
Train station waiting time configuration
Train power emergency cut off button
Train power turn on button
Train control reset button
Train alert indicators display area
Train mode control slider
On Train PLC ID
PLC IP address and port
PLC connection state
PLC output coil state

## Slide 9
Design of the Train Control for Land-Based Railway Cyber Range